## Slide 1
Level 0: uncalibrated data (units of DN) obtained from telemetry packets, that are decompressed and formatted in standard FITS format. The metadata contain only the information that is available from the telemetry packet headers.
Level 1: uncalibrated data (units of DN). The metadata contain extra engineering data from housekeeping telemetry packets.
Level 2: calibrated data (physical units). Corrections for bias, dark current, flat-field, and vignetting, exposure normalisation, pointing, and radiometric calibration are applied. Stokes paramaters, total/polarised-brightness images, polarisation angle/fraction.
All the available orbital and attitude information is used and coordinates expressed in scientific coordinate systems (WCS).
Level 3: science data derived from L2 data, Movies, Carrington maps; and data obtained after scientific analysis, i.e., electron-density maps, solar-wind outflow velocity maps.
Metis data processing levels definition

## Slide 2: Metis Data Level
Incoming data are processed into four Levels: from 0 to 3 (see previous slide).
Level 2 data are processed with current calibration understanding.
Each L2 release comes with a list of known open issues and the recommendation to contact Metis team for support.
The first release L2 data are made available as soon as ready to the Metis science community and to Solar Orbiter scientists, for planning and coordination purposes
The first release L2 data are made available on a public website after 3 months.
All data are reprocessed whenever a new calibration procedure becomes available and immediately released.
Each official release has a DOI that people can cite.
Previous releases remain available.
L3 data will be distributed on a best effort basis together with a processing pipeline
Level 0 and 1 data and HK data are made available upon request.

## Slide 3
Data analysis products and tools
Visible light
  Images of the Stokes parameters, pB (B☉ units), and polarization angle from polarimetric sequences
  Maps of electron density (units: 1/cm3) from polarized brightness (inversion using simple spherically symmetric coronal models – van de Hulst)
  CME tools (TBD)
UV and visible light
  HI Lyman-alpha maps (units: photon/cm2/s/sr)
  Velocity maps (units: km/s) with ne from VL (point [2]) and with simple Doppler dimming models (e.g., set of only 2 coronal HI profiles, one for streamers, another for coronal holes)
Visualization
  Movies (HI Lyman-α and VL)
  Carrington maps from (HI Lyman-α and VL)
Language: Python (TBC)

## Slide 4: Summary of 7th Metis workshop
Synergies with other missions, ground based telescopes and Solar Orbiter payload:
Aditya (Banerjee): VL Coronagraph-Spectrometer: 1.1-3 Rs
ASO-S (Li): Lya/VL coronagraph 1.1-3 Rs
Proba3 (Fineschi): VL coronagraph 1.08-3 Rs
PUNCH (DeForest): VL coronagraph/heliospheric Imager 5 – 45 Rs
UVSC (Fineschi): e- temperature form Thomson scattering of HI Lya
CODEX (Fineschi) – ISS VL coronagraph 3 – 8 Rs
Magnetic field models for PSP (Valori): Connectivity, Magnetic Field extrapolation
PHI (Solanki): magnetometer -> glabal magnetic field
SPICE (Giunta): CME originators, Off-limb spectroscopy: SW vel. Using OVI lines
EUI (Andretta): CME originators, Plume observations at poles
Algorithms for STIX (Massa)
DKIST (Cauzzi): VL Coronagraph/Spectroscopy
K-Cor/UComp (Burkepile): VL Coronagraph/spectroscopy, FOV superposition

## Slide 5: Summary of 7th Metis workshop
Science:
Cosmic rays (Grimani)
CMEs:
  Non-equilibrium ionization effects in CMEs (Pagano)
  Small scale CMEs, Metis visibility (Zimbardo)
  CME shock evidence (Frassati)
  Constraints of models on drag parameters of CMEs (Del Moro)
  FRIS model flux on rope thermodynamics: Metis,SWA (Mishra)
  Spectral lines for CME investigations (Rivera)
  Diagnostics of CMEs (Ying)

## Slide 6: Summary of 7th Metis workshop
Science:
Cosmic rays (Grimani)
Full corona
  Ne models review (1D, 2D and 3D) (Lamy)
  Full solar cycle on UVCS data, (Giordano)
  Image enhancement algorithms (DeForest)
Flux emergence,
  Coronal brightness fluctuations during flux emergence (Guglielmino)
  Blobs in coronagraphic images produced by ricombinations(Papini)
  Impulsive heating and quasi periodic pulsations in loops (Reale)
  Flux rope formation (Romano)
D3 line polarization measurement (Heinzel)

## Slide 7: Topical Teams / Working Groups
CMEs, prominence eruptions, shocks, flux emergence
Global corona (Ne, NH, V, F-corona, Combined Synoptic maps, image enhancements)
Solar Wind
Cosmic rays
Reconnection, plasma fluctuations
Sun-grazing comets
Helium measurements

## Slide 8
FUTURE SCHEDULE (Launch Feb 2020)
2-4 Dec 19 Info Day + Multi-spacecraft investigations of the inner heliosphere: Italian opportunities, ASI, Roma
Dec 19 SVT2
21-23 Jan 20 SOWG#15 CP LTP-2
2-3 Feb 20 SWT#26 CP MLP-3 Jan-Jun 21
5 Feb 20 Launch
Feb-May 20 Commissioning Phase
Jun 20 First STP for Start CP
25 Jun 20 Mission Commissioning Results Review
Oct/Nov 20 8th Metis Workshop (Catania???)